## Slide 1: Chapter 12
How Does the Internet Work?

## Slide 2: ARPA
1969, DoD Advanced Research Projects Agency
Interested in the creation of reliable network

## Slide 3: Initial Four, 1969

## Slide 4: Timeline
http://www.cs.kent.edu/~javed/internetbook/hobbestimeline/HIT.html

## Slide 5: NSFnet 1986

## Slide 6: NSFnet 1991

## Slide 7: Now

## Slide 8: Architecture
Multiple tiers
Backbone
  Long-haul providers

## Slide 9: Tier One Providers
AT&T -- United States
Cogent (formerly PSINet) -- United States
Deutsche Telekom -- Germany
GTT (formerly Tinet) -- United States & Italy
Level 3 Communications (formerly Level 3 and Global Crossing) -- United States
NTT Communications (formerly Verio) -- Japan
OpenTransit (Orange) – France
Sprint -- United States

## Slide 10: Tier One Providers
Tata Communications (Acquired Teleglobe) -- India
Seabone (Telecom Italia Sparkle) -- Italy
TeliaSonera International Carrier -- Sweden & Finland
Verizon Enterprise Solutions (formerly UUNET) -- United States
XO Communications -- United States
Zayo Group (formerly AboveNet) -- United States
Hurricane Electric IPv6 Network -- United States

## Slide 12: NTT

## Slide 13: Underwater Cables

## Slide 14: Level 3 Colorado
Notes: http://maps.level3.com/default/

## Slide 15: You Are Here

## Slide 16: Hierarchy
Notes: https://en.wikipedia.org/wiki/Internet_service_provider
Public switched telephone network

## Slide 17: Coordination
Internet Society (ISOC)
  Internet Architecture Board (IAB)
    Internet Engineering Task Force (IETF)
      Request For Comments (RFCs)
      Standards (STDs)
    Internet Research Task Force (IRTF)

## Slide 18: Coordination
Internet Corporation for Assigned Names and Numbers (ICANN)
  Top-Level Domains (TLDs)
  Independent version of Internet Assigned Numbers Authority (IANA)
  Not associated with US government
Each country controls within their borders

## Slide 19: Addresses
Domain
  Maps via DNS to
IP
  Maps via ARP to
Ethernet

## Slide 20: Domains
Original
  .com, .org, .net, .edu, .gov, .mil
  Two-letter countries: 280
Now
  More specific
  Total of 1082

## Slide 21: Who Are You?
$ whois msudenver.edu
[…]
The EDUCAUSE Whois database is authoritative for the
.EDU domain. Domain Name: MSUDENVER.EDU
[…]
Registrant:
Metropolitan State University of Denver
PO Box 173362
Campus Box 96
Denver, CO 80217
UNITED STATES

## Slide 22: Who Are You?
Administrative Contact:
Mike Hart
Director, Security, Networking, Asset Management, Procurement
Metropolitan State University of Denver
PO Box 173362
Campus Box 96
Denver, CO 80217
UNITED STATES
(303) 556-5074
mhart20@msudenver.edu

## Slide 23: Who Are You?
Technical Contact:
Jesse Nguyen
Manager, Windows Server Administration
Metropolitan State University of Denver
PO Box 173362
Campus Box 96
Denver, CO 80217
UNITED STATES
(303) 556-4683
dnsadmin@msudenver.edu
Name Servers:
NS4.MSUDENVER.EDU 147.153.45.75
NS5.MSUDENVER.EDU 147.153.45.76

## Slide 24: Look It Up
$ nslookup www.msudenver.edu
Server: 8.8.8.8
Address: 8.8.8.8#53
Non-authoritative answer:
Name: www.msudenver.edu
Address: 147.153.45.41

## Slide 25: DNS Root Servers
a.root-servers.net 198.41.0.4, 2001:503:ba3e::2:30 VeriSign, Inc.
b.root-servers.net 192.228.79.201, 2001:500:84::b USC/ISI
c.root-servers.net 192.33.4.12, 2001:500:2::c Cogent Communications
d.root-servers.net 199.7.91.13, 2001:500:2d::d University of Maryland
e.root-servers.net 192.203.230.10 NASA (Ames Research Ctr)
f.root-servers.net 192.5.5.241, 2001:500:2f::f ISC
g.root-servers.net 192.112.36.4 US Department of Defense
h.root-servers.net 128.63.2.53, 2001:500:1::803f:235 US Army
i.root-servers.net 192.36.148.17, 2001:7fe::53 Netnod
j.root-servers.net 192.58.128.30, 2001:503:c27::2:30 VeriSign, Inc.
k.root-servers.net 193.0.14.129, 2001:7fd::1 RIPE NCC
l.root-servers.net 199.7.83.42, 2001:500:3::42 ICANN
m.root-servers.net 202.12.27.33, 2001:dc3::35 WIDE Project

## Slide 26: Root Servers

## Slide 27: DNS Hierarchical
Notes: https://upload.wikimedia.org/wikibooks/en/7/72/Strucutre-of-dns.jpg

## Slide 28: IPv4
32 bits of address
Typically written in dotted octet form
Broken into five classes

## Slide 29: Classes
 | Prefix | NW | Rest | Count | Addresses | Start | End
A | 0 | 8 | 24 | 128 | 16,777,216 | 0.0.0.0 | 127.255.255.255
B | 10 | 16 | 16 | 16,384 | 65,536 | 128.0.0.0 | 191.255.255.255
C | 110 | 24 | 8 | 2,097,152 | 256 | 192.0.0.0 | 223.255.255.255
D | 1110 |  |  |  |  | 224.0.0.0 | 239.255.255.255
E | 1111 |  |  |  |  | 240.0.0.0 | 255.255.255.255

## Slide 30: IPv4 Issues
Not enough addresses
  We’re essentially out
  Underutilized
  Several things have helped
    Network Address Translation
    Classless Inter-Domain Routing
Not easily routable

## Slide 31: NAT
Translate many internal addresses to one or a few external address(es)
Use private IP address ranges internally
  A: 10.0.0.0 - 10.255.255.255
    16,777,216
  B: 172.16.0.0 - 172.31.255.255
    1,048,576
  C: 192.168.0.0 - 192.168.255.255
    65,536

## Slide 32: NAT
Have to map connections via address/port pair
All ISPs do this
The address your machine uses is not what the rest of the world sees

## Slide 33: CIDR
Remove strict 8-bit boundaries to classes
Now can subnet to assign portions of each class
E.g.: 192.193.194.0/28
  Four bits for rest
  16 addresses
    1 each for network (192.193.194.0) and broadcast (192.193.194.15) and gateway (192.193.194.1)

## Slide 34: IP Address in Domain

## Slide 35: ICANN Delegates
AfriNIC (African Network Information Center)
APNIC (Asia Pacific Network Information Center)
ARIN (American Registry for Internet Numbers)
LACNIC (Latin American and Caribbean Internet Addresses Registry)
RIPE NCC (Réseaux IP Européens Network Coordination Centre) assigns and manages IP addresses for Europe, the Middle East, and parts of Central Asia

## Slide 36: IPv6
128 bits
  Approximately 5×1028 addresses for person
  252 addresses for every observable star in the known universe
  Address every atom on the surface of the earth, and still have enough addresses left to do another 100+ earths
  But not all released
Notes: http://itknowledgeexchange.techtarget.com/whatis/ipv6-addresses-how-many-is-that-in-numbers/

## Slide 37: Precisely
340,282,366,920,938,463,463,374,607,431,768,211,456
340- undecillion, 282- decillion, 366- nonillion
920- octillion, 938- septillion, 463- sextillion
463- quintillion, 374- quadrillion, 607- trillion
431- billion, 768- million, 211- thousand
456

## Slide 38: IPv6
Geographic routing
  Route aggregation
Fixed length headers
Jumbo grams/frames
Hexadecimal and colons

## Slide 39: IPv6 Address

## Slide 40: Special IPv6 Addresses
::1/128
  Localhost
fe80::/64
  Link local
ff00::/8
  Multicast
2001::/16
  Unicast assigned to ISPs

## Slide 41: Example
en0: flags=8863<UP,BROADCAST,SMART,RUNNING,SIMPLEX,MULTICAST> mtu 1500
ether a4:5e:60:e8:b9:05
inet6 fe80::a65e:60ff:fee8:b905%en0 prefixlen 64 scopeid 0x4
inet 192.168.1.3 netmask 0xffffff00 broadcast 192.168.1.255
nd6 options=1<PERFORMNUD>
media: autoselect
status: active

## Slide 42: Ethernet Addresses
48 bits
Manufacturers register with Institute of Electrical and Electronics Engineers (IEEE)

## Slide 43: Who Is On This LAN?
$ ping 192.168.1.255
PING 192.168.1.255 (192.168.1.255): 56 data bytes
64 bytes from 192.168.1.11: icmp_seq=0 ttl=128 time=85.006 ms
64 bytes from 192.168.1.6: icmp_seq=0 ttl=80 time=85.151 ms
64 bytes from 192.168.1.4: icmp_seq=0 ttl=64 time=290.633 ms
64 bytes from 192.168.1.11: icmp_seq=1 ttl=128 time=4.172 ms
64 bytes from 192.168.1.6: icmp_seq=1 ttl=80 time=4.490 ms
64 bytes from 192.168.1.4: icmp_seq=1 ttl=64 time=115.507 ms
$ arp -a
? (192.168.1.1) at 74:44:1:45:f6:ab on en0 ifscope [ethernet]
? (192.168.1.4) at a0:99:9b:2:20:65 on en0 ifscope [ethernet]
? (192.168.1.6) at 9c:ad:ef:ff:6:2f on en0 ifscope [ethernet]
? (192.168.1.11) at 0:5:cd:35:aa:65 on en0 ifscope [ethernet]
? (192.168.1.255) at ff:ff:ff:ff:ff:ff on en0 ifscope [ethernet]

## Slide 44: Connecting Laptops
Well, and most other machines too
  Only servers typically don’t have dynamic addresses
Dynamic Host Configuration Protocol (DHCP)
  IP address, gateway, netmask, DNS

## Slide 45: Email
Originally only text
New Multipurpose Internet Mail Extensions (MIME)
Very flexible mechanism for attaching any kind of data
Also used in HTTP

## Slide 46: Uses
Text in character sets other than ASCII
Non-text attachments: audio, video, images, application programs, etc.
Message bodies with multiple parts
Header information in non-ASCII character sets
Notes: https://en.wikipedia.org/wiki/MIME

## Slide 47: Type/Subtype
application/pdf pdf
audio/mpeg mpga mpega mp2 mp3 m4a
image/jpeg jpeg jpg jpe
text/html html htm shtml
video/mpeg mpeg mpg mpe

## Slide 48: Headers
Content-Transfer-Encoding
  Base 64
Content-Type
  multipart/alternative
  multipart/mixed

## Slide 49: Trusting Email
Don’t
Pretty much everything can be faked
Exception: digital signatures
Pretty Good Privacy
  Gnu Privacy Guard
  https://gpgtools.org/
  https://www.enigmail.net/home/index.php
  http://gpg4win.org/

## Slide 50: Email Delivery
Many viruses have been sent via email
Turn off all processing in your reader
  Don’t automatically open apps
  Maybe don’t show images

## Slide 51: How They Get Our Address
Web page scraping
Google
Signing up
Selling of lists
Good guessing
  admin@

## Slide 52: Fighting SPAM
Alternate email addresses
  For the various sites you sign up for
  One you always ignore
  Gmail: your.username+any.alias@gmail.com
White list those you know
Filter requiring interaction
Notes: https://support.google.com/mail/answer/12096?hl=en

## Slide 53: Fighting SPAM
Heuristics for recognition
  More than N recipients
Click on “SPAM” button
  Crowd sourcing
https://www.spamcop.net/
https://www.spamhaus.org/

## Slide 54: Review
Questions: 3, 7, 10
Exercises: 2, 3, 6