## Slide 1: Chapter 9
How are Computers Connected?

## Slide 2: Wires
Need at least two wires
  Electricity must flow
  Typically insulated
  Often twisted
Ground
  Alternate electrical path
  In case of internal shorts

## Slide 3: Twisted Pairs
Helps reduce interference
  Differential mode signaling
Invented by Alexander Graham Bell
Telephone and Ethernet cables
Notes: https://en.wikipedia.org/wiki/Twisted_pair

## Slide 4: Jacks
Registered Jack “RJ”
RJ-11 for telephones
  Two wire: tip and ring
  ~50 volts
Installation is expensive, wire is cheaper
  Usually four or six wires run to each socket

## Slide 5: Jacks
RJ-45
  Ethernet
  Eight wires
  Four pairs

## Slide 6: Cats
Categories for cables
  Cat 1 – telephone
  Cat 5 – unshielded twisted pair
    Up to 1000BaseT
    Cat 5e should have better crosstalk rejection
  Cat 6 – up to 10GBaseT
    10 Gigabits, baseband signaling, twisted pair
Book is off on the speeds, page 250

## Slide 7: Crossover
Historically, one could connect two computers via a crossover cable and no hub/switch
Required the use of a crossover cable
These days, the network interface cards (NICs) recognize the signaling difference and do the right thing

## Slide 8: Universal Serial Bus
1.0: 1.5 – 12 Mbps
2.0: 480 Mbps
3.0: 5 Gbps
Backwards compatible

## Slide 9: Connections
Point to point wiring quickly become untenable
  O(n2) connections
Star network
  All components connected to central controller
  Telephones in a company
    Private Branch eXchange (PBX)
    Wiring closets
  Each new connection requires one wire

## Slide 10: Architectures

## Slide 11: Ethernet
A single shared bus
  Broadcast
No need for centralized controller
  Uses distributed control
  No single point of failure
All communications seen by all machines
Header contains information about source and destination machines

## Slide 12: Network Stack: OSI Model

## Slide 13: Network Stack: Protocols

## Slide 14: Network Stack: Peering Layers

## Slide 15: Network Stack: Headers & Chksum

## Slide 16: Network Stack: The OS View

## Slide 17: Ethernet
Rules determine who can transmit
Listen before speaking
Still can collide as two can start at the same time
  And there is delay
  Listen while speaking
If collide, wait for a random amount of time and try again

## Slide 18: Ethernet
Limited maximum amount of data transferred
  ~1500 bytes
  ~9000 bytes for jumbo frames

## Slide 19: Hubs
Typically machines are connected to a hub or switch
  Helps with the electrical characteristics
Hub works at the physical layer
  Broadcast

## Slide 20: Switches
Link layer
  Typically, only the two machines involved see their traffic
  Can reduce congestion
  Switches learn the addresses of the connected machines
Routers work at the internet layer

## Slide 21: Token Ring
Machines wired in a ring
Information circles the ring
To transmit, a machine has to capture the token
  A specific bit pattern
  Machine removes bit pattern and transmits data
  No collisions, better under load

## Slide 22: Token Ring
When data addressed to machine, it drains the data
  And puts token back on
  Sharing occurs around the ring
If originating machine see the data it sent, knows the destination machine did not get the data

## Slide 23: Wireless
Similar to Ethernet
  Broadcast, small packets, single talker
Somewhat more complicated
  Multiple access points visible
  Electrical interference
  Laptops move from one LAN to another

## Slide 24: Example

## Slide 25: Access Points
Identified by Service Set IDentifier (SSID)
  Frequently randomly broadcast
To connect, machine sends association message
  Might require credentials
  Hopefully encrypted
Variety of speeds
  54, 11, 5.5, 2, 1 Mbps

## Slide 26: Hidden Machine Problem
Two machines might see AP, but not each other
  Out of range of signals
Machine must request to send and receive confirmation

## Slide 27: Ad Hoc
Machines can form networks to talk to each other even if not connected to internet
Zero configuration LAN
IP addresses typically start with 169.254
Each machine picks a random address and asks if any other machine already has that address

## Slide 28: Review
Questions: 8
Exercises: 2, 3